## Slide 1: Channel Archiver
Oct 2000
Kay-Uwe Kasemir, LANL

## Slide 2: Channel Archiver
Generic archiving system for EPICS
Stores independent “Channels” = any Process Variable served by Channel Access
Sampling options
  a) periodically
  b) on change

## Slide 3: Goals
Fast:
  Hash-table channel lookup, binary data format with direct access to recent values.
Generic and Portable:
  Win32, Linux, Solaris, HPUX,…
  Data archived: EPICS dbr_time_*, providing system-independent access to float, int, string, enum, … with time & status, units, limits, …
Networked:
  Remote access to both Engine status/configuration and archived data
Extendable:
  I/O library meant to be extended to make Engine, CGI Tool etc. work with different storage formats
Attractive for both casual users and “experts”
  Web interface, Win32 archive viewer for generic access to raw samples
  scripting support (SWIG) for automated analysis, creation of input for other programs

## Slide 4: Components
Engine: Taking data from ChannelAccess
CGIExport: Web access to data
ChannelArchive ScriptingInterface: SWIG access for more sophisticated analysis
WinBrowser: Win32 tool for fast archive browsing
Archive I/O library: portable archive I/O, extendable for different file formats

## Slide 5: Interactions
Workstation
CA Server
CA
Network
Viewer
I/O Lib
Engine
I/O Lib
CA
Scripting
I/O Lib
Web Browser (data)
HTTP
HTTP
Web Browser (Engine cfg.)
Web Server
I/O Lib
CGIExport
HTTP
HTTP
HTTPD
IOC
EPICS Db
CA

## Slide 6: Engine
Networked via HTTP
Up to 10000 values/sec (450Mhz PC)
WIN32, Linux, Solaris

## Slide 7: Engine: Start
USAGE: ArchiveEngine [Options] <config-file> [<directory-file>] Options: -port <port> WWW server's TCP port (default 4812) -description <text> description for HTTP display -log <filename> write logfile Default directory-file: 'freq_directory'
Engine is ChannelAccess client: may have to set
  EPICS_CA_ADDR_LIST, EPICS_CA_SERVER_PORT
TCP port has to be unique per machine
Log-file: copy of messages/warnings

## Slide 8: Engine: Configuration
ASCII File:
# Comments
!default_period 30
!group <Another config. file>
  For building disabling groups, otherwise like an #include in C/C++
<Channel Name> <Period [sec]> [Monitor] [Disable]
  Scan period is also important for “Monitor” channels: It determines size of buffer. If more samples arrive than anticipated, “overwrites” occur.
Example: #Archive channels of example CA server (excas) fred Monitor freddy Monitor jane 5 janet 10

## Slide 9: Engine: Groups
“disabling” channel !=0  group disabled:
Main: # Main archive file !default_period 30 !write_period 60 !group power_supply !group another_subsystem
power_supply: # Power Supply: # Archive only when power is on! power_off Monitor Disable power_setpoint power_readback power_temperature

## Slide 10: Engine: More Options
!write_period <seconds> Time between writes to disk
!get_threshold <seconds> Internally, CA ‘get’ is used for channels scanned at period > threshold, remaining channels are ‘monitored’
!buffer_reserve Engine keeps memory buffer per channel to buffer between writes to disk. Size: buffer_reserve * write_period/scan_period Since writes can be delayed by other tasks, disk activity etc., buffer is usually bigger than the minimum required (default: 3). If receiving "override" messages, one should
  Check if the offending channel is tagged Monitor. In that case the period estimate might be too large.
  Increase buffer_reserve (global for all channels)

## Slide 11: Engine: Status
URL of engine’s HTTPD: http://<machine>:<port>
“Client Pull”: Updates on reload
Changes (added groups/channels) written to cfg subdirectory, original config. files unchanged

## Slide 12: Engine: Sampling
Original time stamps of CA Server / IOC preserved, not adjusted/rounded to period!
Example: “1.0 sec”
 every sec., last value is saved

## Slide 13: WIN32 Browser
Familiar User Interface
Win. Only

## Slide 14: XARR, StripTool (Chris Larrieu, JLab)
View/Export Tools for UNIX (X11/Motif)
XARR: access to archive via older lib.
Plan: Support LibIO for both

## Slide 15: CGIExport
For any Web Browser, any Web Server w/ CGI
Archive Info
Simple Plots (GNUPlot)
Export in Spreadsheet format
Web Server
I/O Lib
CGIExport
HTTP

## Slide 16: CGIExport: Plots

## Slide 17: CGIExport: Spreadsheet Options
Original Time Stamps: ill-suited for Spreadsheets
“Fill” missing values by repetition
Linear Interpolation for given period
(initial #N/A until all channels have valid value)

## Slide 18: CGIExport: “Fill”, “Interpol.”, ...

## Slide 19: Scripting Interface
Not optimal for “end users”, but allows programmers to
  provide adjustable scripts: Time/Y Plot, X/Y Plot, List,...
  automatically generate e.g. daily statistics for Web
  write filters for Matlab, Mathematica, …
  answer questions like: “How often was XX below 10.0 and for how long?”

## Slide 20: CASI: Channel Archive Scripting Interface
SWIG - based:
  allows access from tcl, perl, python
  available for Win32 and Unix
  Available Examples: tcl/tk and python
  for Win32 and Linux: loadable module
API:
  Plain adaption of ChannelArchive LibIO

## Slide 21: Generic Examples

## Slide 22: Channel Archiver LibIO
Portable C++ code (handling e.g. byte swapping)
Based on generic “Iterator” interface:
  Archive: list channels
  ChannelIterator/Channel: first/last time available, find value before/after/near time
  ValueIterator/Value: get time, status, value both as string and “raw”
Supported: BinArchive, MultiArchive

## Slide 23: LibIO: Example
#define ARCHIVE_TYPE BinArchive
void list_values (const stdString &archive_name, const stdString &channel_name, const osiTime &start, const osiTime &end)
{
Archive archive (new ARCHIVE_TYPE (archive_name));
ChannelIterator channel(archive);
ValueIterator value(archive);
if (! archive.findChannelByName (channel_name, channel))
return;
channel->getValueAfterTime (start, value);
while (value && value->getTime() < end)
{
cout << *value << endl;
++ value;
}
}

## Slide 24: BinArchive File Layout
Directory File
Disk-based Hash Table
Channel “X”
start time
end time
first data buffer
last data buffer
Channel “Y”
start time
end time
first data buffer
last data buffer
Data File 1
Control Info units, limits, ...
Data Buffer (X)
buffer info: start/end, type, …
prev buffer, next buffer
{ Samples }
Control Info units, limits, ...
Data Buffer (Y)
buffer info: start/end, type, …
prev buffer, next buffer
{ Samples }
Data Buffer (Y)
buffer info: start/end, type, …
prev buffer, next buffer
{ Samples }
Data File 2
Control Info units, limits, ...
Data Buffer (X)
buffer info: start/end, type, …
prev buffer, next buffer
{ Samples }
Control Info units, limits, ...
Data Buffer (Y)
buffer info: start/end, type, …
prev buffer, next buffer
{ Samples }

## Slide 25: BinArchive Features
Hash Table
  fastest lookup by name
  less suited for sorted listing or wildcard lookup
Binary Data File, Multiple Channels per File
  minimized open/close calls, fastest read/write access
  byte swapping required, harder to maintain
Double-Linked Data Blocks
  fastest access to most recent values
  links must not be broken

## Slide 26: ArchiveManager Program
Extraction of channels and time range into new archive
  attempt is made to skip/repair “broken” values while copying
Channels/time ranges can be appended to existing archive
  no “insert” nor “prepend”!
Possible Approach:
  Create extracts of reasonable size for backup (e.g. monthly CD-ROM)
  Original archive can be recreated from extracts, starting with the oldest one, not going back in time
1999
(copy)
1999
(orig.)
Jan.’99
Feb.’99
Mar.’99
Dec.’99
...

## Slide 27: MultiArchive
Allows read-access to list of archives
  compile-time option for CGIExport, Tcl extension, WinBrowser
  first archive that holds requested data is used
  when iteration meets end of data, archive list is searched again
  no sophisticated merging, i.e. archives should not overlap in time
  for now each individual archive has to be a BinArchive
Format: # ChannelArchiver master file master_version=1 # Order in which archives are checked for data: /archives/fast/dir /archives/main/SinceJan2000/freq_directory /archives/main/Jul99-Dec99/freq_directory /archives/main/Jan99-Jun99/freq_directory /home/fred/xyzarchive/dir

## Slide 28: More Information
“ChannelArchiver” under http://mesa53.lanl.gov/lansce8/epics/PC
Documentation is part of sources: ChannelArchiver/doc
Bob Dalesio: ldalesio@lanl.gov Kay-Uwe Kasemir: kasemir@lanl.gov